## Slide 1: Online event filtering and data acquisition at J-PARC-HI Hiroyuki Sako (JAEA / U. Tsukuba) ミニワークショップ: 次世代物理実験に向けた広帯域データ収集・処理システム 2020/3/16 at Tokyo Office of U. Ryukyu
Outline
Overview of J-PARC-HI
Required performance of online trigger and DAQ
Issues
Notes: It is my pleasure to show a future plan of J-PARC heavy-ion program in this QM conference at Kobe.
The out line of my talk is as follows.

## Slide 2
HI linac & Booster
Proven performance of high-intensity
Proton acceleration
Introduction of HI injector
High-density frontier
Quark/nuclear matter
Hadron/strangeness research with high-intensity frontier beams
J-PARC (High intensity proton synchrotron facility

## Slide 3: Strategy towards J-PARC-HI experiment
Extended area
Hadron Experimental Facility
3. J-PARC-HI Main experiment
Large acceptance high-rate spectrometer
(up to 1011 Hz HI beams)
2. J-PARC-HI Pilot run
Upgraded E16
Low-rate HIC (up to ~108 Hz HI beams based on radiation dose estimation)
１．p+A experiment (E16) (Apr. 2020-)
Baseline data and detector R&D for HIC
High-p extended beamline
High-p beamline
Hadron Exp. Facility (present)
Extended facility (planned)
Notes: We show here the strategy towards the J-PARC-HI experiment
We will perform from next Feb, p+A experiment (E16), by using the proton
Beam transported with the high-momentum beam line, where we measure baseline
Data and perform detector R&D for HIC.
Next, after we realize the HI acceleration, we perform the J-PARC-HI pilot run
Using the upgraded E16 spectrometer, and the HI beam rate of up to 108 Hz
Transported to the same beam line
Finally we perform main experiment with large acc high-rate spectrometer
up to 10^11 HI beam with the extended beamline
From now we first show the main exp, pilot run, and p+A experiment.

## Slide 4: Goals of J-PARC-HI (I)
  Search for QCD Phase structures
    1st order phase transition, QCD Critical Point
  EOS of dense matter
    Structure of neutron stars
  Chiral symmetry restoration
    Medium modification of vector mesons
  High-density event trigger
    Large e-b-e fluctuations of max. density
    Higher statistics  Higher density events
4
Hadron
QGP
1st-order
phase boundary
QCD Critical Point
Color
Super
conductor
J-PARC-HI
STAR-BES
FAIR
NICA,…
QCD Phase diagram
Exploring dense matter
Neutron Star
and merger
LHC/
RHIC
Sum of hadron pT

## Slide 5: Goals of J-PARC-HI (II)
5
  Efficient production of strangeness at J-PARC
  Search for rare multi-strangeness systems
    Hypernuclei, strangelet, dibaryons, etc.
  Study of hyperon interactions
    Two-particle correlations
    EOS of strangeness matter
Studies of multi-strangeness production
J-PARC-HI
Hypernuclei
J-PARC-HI
LL correlation function
QS+BB interaction
10
102
103
√sNN (GeV)
A. Andronic, PLB697 (2011) 203
A. Andronic, et al, Nucl. Phys. A 837 (2010) 65
√sNN (GeV)
103
10
102
STAR, PRL114 (2015) 022301

## Slide 6: Goals of J-PARC-HI
  Search for QCD Phase structures
    1st order phase transition, QCD Critical Point
  EOS of dense matter
    Structure of neutron star
  QCD vacuum property
    Chiral symmetry restoration
6
Strangeness physics
Hadron
QGP
1st-order
phase boundary
QCD Critical Point
Color
Super
conductor
J-PARC-HI
QCD Phase diagram
Exploring highest density matter
Initial Universe
Neutron Star
and merger
LHC/
RHIC
  Search for new multi-strangeness system
    Hypernuclei, strangelet, dibaryons, etc.
  Study of hadron interactions
    EOS of strangeness matter
Strangeness factory

## Slide 7: J-PARC-HI: High-intensity Frontier
Strangelets: P. Braun-Munzinger,
J. Phys. G21 (1995) L17
Statistics
1 year at AGS = 5 min at J-PARC-HI
世界最高強度 ~1011 Hz, 反応レート = 108 Hz
Elab=1-11AGeV, sNN=1.9-4.9GeV （陽子30GeV相当）
  将来的に19AGeV, 6.2 GeV （陽子50GeV相当）のアップグレード検討
イオン種: p, ..., Au, U
Ref: HSD calculations in FAIR Baseline Technical Report (Mar 2006)
A. Andronic, PLB697 (2011) 203
Beam rate: 1011 Hz
0.1% lI target
Interaction rate: 108Hz
In one month experiment:
r,w,fee: 1010 - 1012
Hypernuclei: 104 – 1012
J/Y, D : 107-109
Strangelets: 1 - 102
Highest baryon density
Max baryon density
High rate beam * fixed target
World’s highest interaction rate : 108Hz
5-order higher than AGS / SPS
AGS, SPS
1 year
J-PARC-HI
5 min
＝
1-order higher than FAIR

## Slide 8: J-PARC-HI 計画 - 宇宙最高密度物質の研究 -
J-PARCにおける重イオン衝突
原子核の８倍程度の宇宙最高密度の物質を生成する唯一の実験的手段
研究目的
強相互作用物質の相構造の解明
(一次相転移境界線、臨界点）
高密度物質の物性研究（状態方程式等）
2025年頃の開始を目指す
LHC
RHIC
GSI-SIS
mB
J-PARC
臨界点
初期宇宙
原子核
NS-NS merger
中性子星
星
超新星爆発
ハドロン・原子核物質の相図
Notes: As you all know, at RHIC and LHC, QGP has been discovered at high temperature and low density.

## Slide 9: HI Beams at J-PARC-HI
Strangelets: P. Braun-Munzinger,
J. Phys. G21 (1995) L17
Statistics
1 year at AGS = 5 min at J-PARC-HI
World’s highest beam rate ~1011 Hz, Interaction rate = 107-8 Hz
Elab=1-19AGeV, sNN=1.9-6.2GeV (U)
Ion species: p, Si,…, Au, U
Ref: HSD calculations in FAIR Baseline Technical Report (Mar 2006)
A. Andronic, PLB697 (2011) 203
Beam rate: 1011 Hz
0.1% lI target
Interaction rate: 108Hz
In one month experiment:
r,w,fee: 1010 - 1012
Hypernuclei: 104 – 1012
J/Y, D : 107-109
Strangelets: 1 - 102
Highest baryon density
AGS

## Slide 10: Particle production rates
Beam : 1010 Hz
0.1 % target
 Min-bias event rate 107Hz
In 1 month experiment:
r,w,fee 109-1011
Hypernuclei 103 -1011
HSD calculations in FAIR Baseline Technical Report (Mar 2006)
A. Andronic, PLB697 (2011) 203
Dilepton
Hypernuclei
AGS
Strangelets: P. Braun-Munzinger J.Phys.G21 (1995)L17
10-13 sensitivity at J-PARC

## Slide 11: Hadron setup
Identified charged particles
~4p acceptance
  Silicon Pixel Tracker (SPT) (q < 4o)
  TPC (q > 4o)
  MRPC-TOF
Interaction Rate : <=1 MHz
  Triggerless DAQ system
Centrality : Multiplicity counter + Zero-degree calorimeter
Samurai
Magnet
B=3.08T,BL=7.05Tm
ZCAL
TPC
SPT
Target
Magnet yoke
Top view
2m
4o
MRPC-TOF
3.4m
2m
Neutron counter
3.5
2.75m
45o
1.5
Charge
veto
B=1.5T
MC
E
B=1.5T
Beam view
Magnet pole
2
2
3.4
5.6
3
38.7o
41.4o
6.8
y-pT Acceptance
PID with TOF
Dimuon Setup
Replace TPC by:
  Pb absorbers and GEM trackers
  7-layer forward and barrel Silicon Pixel Trackers
Interaction Rate : 10 MHz
SPT
4o
0.6
0.6
Pb absorber
GEM
trackers

## Slide 12
Simulation
~1200 charged particles are produced in U+U collisions

## Slide 13: Problem
Zero-suppression/clusteringFPGA?
Tracking/Event selection GPU or CPU?
Zero suppression
Peak finding/clustering
Tracking
Save only tracks on disk
pad
Detectors
Target
Beam
No. of tracks ~1200
4. Event separation and selection
Analysis of track information
waveform

## Slide 14: Data rate estimation
  Multiplicity per detector plane (GEM trackers only)
    Central 6.5% U+U at 10 AGeV/c
  Data rate
  R = NRISDe
  = 4.6 TB/s
Detector | No. of Plane | No. of hits
TPC | 117 | 575*117
SPT | 4 | 575*11
TOF | 3 | 575*7
Total |  | 67275
Parameter | No. of Plane | No. of hits
RI | Interaction rate | 107Hz (MB)/105Hz(1% Central)
S | No. of pads per hit | 2
D | Data size / pad | 4B (TDC/ADC/address)
e | Efficiency | 0.8

## Slide 15: Comparison with ALICE
Multiplicity, event rate
Comparable data rate : several TB/s
Periodic interaction (ALICE), random interaction (J-PARC-HI)
 | J-PARC-HI | ALICE
Multiplicity (charged,4p) | ~1200 | 21400
Collision rate | 10 MHz | 50 kHz
Data rate | ~4.6TB/s (after zero suppr) | ~3.3TB/s

## Slide 16: Details
Ion-Ion interaction rate = 10MHz
Occupancy (Hit probability per event in each pad) = 10%
Signal rate in each pad = 1MHz↔1ms
ts : Shaping time <= 100ns
Sampling frequency (1/Dt) >= 50MHz (ALICE SAMPA = 5MHz)
ts
Dt

## Slide 17: Concept of Online-Offline computing system for J-PARC-HI
FPGA
Detectors
(SPT, TPC,
TOF,…)
Data link
Zero suppression
Clustering
Tracking
Event reconstruction
/filtering
FPGA
CPU
memory
PCIe
GPU
CPU
memory
Network links
Network switch
PCIe
1TB/s
(digitized waveform data)
10GB/s
(to SSD/HDD)
1ms/event/PC
→1MHz event rate / 1000PC
Event filtering (semi-online trigger)
With global detectors
(MC, ZCAL, etc)Cuts in timeframe
1st stage PCs (FLP)
2nd stage PCs (EPN)
100GB/s
(Selected events)
Front-end
Electronics
(continuous
Readout)

## Slide 18: Two-event resolution for J-PARC-HI
Assumptions
Consider only particles with b>0.5
Rough estimation of Two-event resolution
(~TOF difference of b=0.5-1 particles of 2 events)
  Z=0.3m (outer vertex detector), dt=1ns (c=0.3m/ns)
  Z=2m, dt=6.7ns
  Z=5m (TOF position), dt=16.7ns
   Maximum hit rate = 60MHz
  Maximum event rate = 600MHz (10% occupancy)
Requirement for 600MHz event rate
Compact detector (z<5m)
Fast response (<17ns)
Sampling frequency larger than 60 MHz
As many detector planes as possible
4-d (t,x,y,z) tracking and fast primary vertex reconstruction to reject overlapping events
t(ns)
30
z(cm)
1
2
3
Waveform at each detector plane
Overlap of hits
from 2 collision events
ev1
ev2
b=1
b=0.5
0
Slowest
in ev1
Fastest
in ev2
Dt
Vertices

## Slide 19: Wish list for J-PARC-HI
Online clustering in TPC
Online track reconstruction in SPT, TPC, TOF
  Track
  Momentum
  TOF
Software Triggers (Event filtering)
  Centrality trigger (Zero-degree calorimeter and Multiplicity Counter)
  Sum of transverse momenta (TPC)
  No. of identified particles (p, pi+-, K+-,…) (TPC, TOF)
  Dimuon trigger (SPT and Muon Tracker)
  Rare particle trigger (Track reconstruction and secondary vertex reconstruction in TPC)
    Ω-→K-Λ→K-π-p, Dilepton at high mass (e.g. J/ψl+l-), (anti-)hypernucleiπ- + nuclei, …
Rejection of pileup events
  4-d online tracking and vertex reconstruction in SPD
Online Data reduction: 5 TB  50 GB?
What is the optimum system configuration to achieve these?

## Slide 20: Backup

## Slide 21: J-PARC E16 : Dilepton in p+A (Feb. 2020-) f meson modification in nucleus
30 GeV proton beam at 1010 / spill
High momentum beam line
Pb target
Proton
Cu
e+e- invariant mass
KEK-E325
HBD
GEM Trackers
RPC-TOF
fK+K-

## Slide 22: Status of J-PARC E16 Run 0
Installation of LG, HBD, GTR
R&D for MRPC for hadron measurement
Run 0 in Feb. and Oct. 2020
First dielectron measurement in p+C/Cu and commissioning of MRPC
MRPC-TOF
RUN 2
RUN 1 (2022)
RUN 0 (2020)

## Slide 23: RPC at E16
Event start counter (R~1700mm)
MRPCs
3 or 4 RPCs will be available for Run 0 (Feb-Mar 2020)
  3 borrowed from BGOegg, one may be newly produced
10 RPCs in total in the future (at two 30-deg Sections)
Track start counter
R=100-200mm

## Slide 26
2016計測システム研究会at J-PARC, T. N. Takahashi

## Slide 29
X
X
X
(X)
X
, clock
X不具合
X
HDDAQ
GPIO
▲不整合
(未)

## Slide 34: HUL(Hadron Universal Logic)-TDC (steaming readout mode) R. Honda (Tohoku U.)

## Slide 35: Beam Test at ELPH (Tohoku U)
3MHz e+e- beams
Scintillating fiber (128ch)
Scintillation counter (14ch)
Drift chamber (30ch)
1/100 scale of E50 detector system
Highest throughput data in each network link achieved
Switch-DAQ-PC (10Gbps x 1)
TDC –Switch (1Gbps x 6)

## Slide 37: Hypernuclear Setup
Closed geometry : Sweeping magnet and Collimator
Limit the acceptance to beam rapidity
Only beam and fragments can reach 2nd dipole magnet
Lifetime and Magnetic moment of hypernuclei
Search for new hypernuclei and strangelet
Interaction Rate : ~100 MHz
Samurai
Magnet
B=3.08T,BL=7.05Tm
TPC
SPT
Top view
2m
4o
MRPC-TOF
0.5
3.4m
3.5
45o
1.5
B=1.5T
Collimator
Sweeping magnet (5T)
2.4m
Decay of Hyper
nucleus
p-
fragment
Target
Beam
Horizontal Position
∝Z/A
H. Tamura, J-PARC-HI Workshop (2018)
Slit

## Slide 38
U+U衝突において
約1200個の荷電粒子が発生

## Slide 39: HI acceleration scheme at J-PARC
3 GeV RCS
(p)
0.4  3 GeV
MR
330 GeV (p)
H- Linac: 0.4 GeV
MLF
proton (existing)
U92+
 11.2 AGeV
p/HI
HI (under plan)
U86+
 735 AMeV
stripping
HI beam rate ~1011 Hz (World’s highest expected)
Elab (U) = 1-19 AGeV (Phase I: 1-12 AGeV)
sNN (U) = 1.9-6.2 GeV (Phase I: 1.9-4.9 GeV)
U66+
 67 AMeV
stripping
HI Linac
HI Booster Ring
Hadron Experimental
Facility
Proton beam rate (slow extraction)
5.5x1013/cycle (currently)
1.2x1014/cycle (2022)
このエネルギーがどのような
領域か？
Proton operation
since 2006
Full setupでの物理を強調

## Slide 40: Data flow & processing (1)
O2/T0/T1
FLPs
EPNs
FLPs
Detectors electronics
Detector data samples
synchronized
by heartbeat triggers
Buffering
TPC
Detector reconstruction
e.g. track finding
Raw data input
Data Reduction 0
e.g. clustering
Local processing
Time Frame building
Frame dispatch
Global processing
TRD
Sub-Time Frames
Partially compressed
sub-Time Frames
Full Time Frames
Compressed Time Frames
Data Reduction 1
…
Trigger and clock
Calibration 0
on local data,
ie. partial detector
Calibration 1
on full detectors
e.g. space charge distortion
T0/T1
Archive
Time slicing
O(100)
O(1000)
Local aggregation
Storage
Quality Control
Sub-Time Frames
Time Frames
Compressed Time Frames
AOD
QC
QC
Tagging
Synchronous
QC data
ITS
…
CTF
AOD
Storage
Load balancing & dataflow regulation
First-Level Processors (FLPs)
Event Processing Nodes (EPNs)
ALICE-O2 data flow
Time frame (events) building
CRU
(FPGA board)
CPU+
GPU

## Slide 41: The receiver cards
C-RORC
12 bidir. links @ 6 Gb/s
PCIe gen2 x8
2 x RAM SLOTS
FMC connector
XILINX VIRTEX6 FPGA
CRU (Common Readout Unit)
48 bidir. links @ 10 Gb/s
PCIe gen3 x16
ALTERA ARRIAX FPGA
F. Costa, Asian O2 workshop (July 2016)

## Slide 42: FLP-PC Prototype （科研費挑戦的萌芽）
A FLP-PC installed at U. Tsukuba
Common FLP-PC shared with remote institutes in Japan
Aimed at DAQ test and performance evaluation between C-RORC to FLP-PC
Specifications
  ASUS ESC4000-G3
  2 x Xeon 8-Core E5-2630v3
  64GB memory
  5TB HDD+128GB SSD
  GPU board : ASUS GTX1070-8G [PCIExp 8GB]
C-RORC borrowed from CERN
CRU to be bought (2018?) SAMPA to be borrowed or bought (2018?)
C-RORC
GPU

## Slide 43: Hardware Facility for ALICE
Detectors
9000 Read-out Links
270 FLPs
First Level Processors
1500 EPNs Event Processing Nodes
Input: 270 ports
Output : 1500 ports
3.3 TB/s
Switching
Network
500 GB/s
90 GB/s
68 Storage Arrays
34 Storage Servers
Storage
Network
Input: 1500 ports
Output : 34 ports
~10GB/s/FLP
~0.3GB/s/EPN
ALICE実験の場合（10億円規模？）
J-PARC-HIでも同規模の計算機ファームが必要
もっとコンパクト、低コスト（数億円）にできないか？
実際に必要な計算機リソースの定量的評価が必要

## Slide 44: J-PARC-HIでALICEのO2が適用可能か？ J-PARC-HIのレート考察
10Hz
(time frame)
ALICEの衝突レート：最大 50 kHz
J-PARC-HIの衝突レート： 最大10MHz
平均100ns間隔の2つの衝突事象のより分けを（onlineで）行う必要がある
  標的から最下流の検出器までの飛行時間は、光速の粒子で、17ns
  100nsでは遅い粒子は前後の衝突事象の粒子とoverlapし始める
TPC SAMPAでは
Shaping time 80/160ns
Sampling frequency (1/Dt)= 5MHz
  200ns time resolution
J-PARC-HIの要求
Shaping time <=10ns
Sampling frequency = 50MHz
……
Digitized ADC data (sampling freq=5MHz)
Heartbeat triggers
(aligned to sampling freq)
ts
Dt

## Slide 45: Prototype test? （科研費萌芽）
Hardware
  FPGA (Altera, OpenCL)
  GPU (NVIDIA, CUDA)
  Host PC (CentOS)
Process simulated waveform data on FPGA memory
  Simulated ion-ion collision data (event generator + GEANT4)  convert hits on each detector into raw waveform data
  Zero suppression and Clustering in FPGA
  Tracking on GPU
  Event selection on CPU
    Resolution of overlapping events
PC
GPU
PCIe
FPGA
Memory
CPU

## Slide 46: まとめと課題
J-PARC Heavy-Ion Project (J-PARC-HI)
  Very high rate interaction rate : 10MHz
  Raw data rate : ~1TB/s
Considering DAQ-O2 system based on ALICE
  Continuous triggerless readout
  Online clustering/tracking/event selection to reduce data from 1TB/s to 10GB/s
  Reduction of the system highly desirable with FPGA and GPU
Prototype test
  ALICE Prototype
    SAMPA + FLP-PC with C-RORC/CRU
  Small scale prototype with simulation data
    PC + FPGA + GPGPU

## Slide 47: Backup

## Slide 48: Software triggers
Event selection with one or two detectors
  Centrality (no. of hits in SVT and ADC sum of ZCAL)
  Dimuon tracks after muon absorber
Semi-online trigger (selection of time frames) before track reconstruction?
Tracking / momentum reconstruction
  Multiplicity of charged particles
  Multiplicity of identified particles
  Sum of transverse momenta
Intelligent trigger (track reconstruction required)

## Slide 49: ALICE O2 upgradeの概要
New computing system
Read-out the data of all interactions
Compress these data as much as possible online (to a few %) by online reconstruction
One common online-offline computing system: O2
Baseline correction and zero suppression
Data volume reduction by zero cluster finder. No event discarded.
Average compression factor 6.6
Unmodified raw data of all interactions shipped from detector to online farm in triggerless continuous mode
Asynchronous (few hours) event reconstructionwith final calibration
HI run 3.3 TB/s
Data Storage: 1 year of compressed data
Bandwidth: Write/Read 90 GB/s
Capacity: 60 PB
90 GByte/s
Tier 0, Tiers 1 and
Analysis Facilities
20 GB/s
Data volume reduction by online tracking. Only reconstructed data to data storage.
Average compression factor 5.5
500 GB/s
90 GB/s
要求
LHC min-bias Pb-Pb at 50 kHz (#track ~ 3000) ~100 x more data than Run 1
Physics topics for ALICE upgrade
  Rare processes( i.e. J/psi, D decays at )
  Very small signal over background ratio
  Needs large statistics of reconstructed events
  Triggering techniques very inefficient
50 kHz > TPC inherent rate (10kHz = drift time ~100 µs) Support for continuous read-out (TPC)
First Level Processor (FLP)
Event Processing Node (EPN)

## Slide 50: Rapidity and pT distributions
10AGeV/c
5AGeV/c
1AGeV/c
1回のU+U衝突当たり
1200個の荷電粒子
が生成

## Slide 51: Pixel size at 10% occupancy at 1 m distance from the target
SSD: Z=2.5cm, minimum pad size = 75x75mm2
GEM tracker : Z=1m, minimum pad size=3x3mm2

## Slide 52: The data stream
F. Costa, Asian O2 workshop (July 2016)

## Slide 53: Experimental challenges
High rate capability
  Fast detectors
    Silicon Vertex Detectors, GEM trackers, …
  Extremely fast DAQ of 10-100MHz
     Triggerless continuous readout + online data reduction
Large acceptance (~4p)
  Rapidity dependence of e-b-e fluctuations
Toroidal magnet spectrometer
  (CBM<30o, beam energy>=8AGeV/c)

## Slide 54: R&D status
Fast Data Acquisition System
  Participation in ALICE-Online-Offline Computing (O2) (RIKEN, Nagasaki IAS, CNS U. Tokyo, U. Tsukuba)
  Continuous triggerless readout, online clustering/tracking
Detectors
  MRPC-TOF (JAEA, U. Tsukuba, KEK)
    Aimed for 60ps time resolution, test with hadron measurements in p+A at J-PARC E16
Theory : Development of dynamical model at J-PARC energy
  M. Kitazawa, T. Hirano, A. Ohnishi, Y. Nara, C. Nonaka, Y. Akamatsu, K. Morita, …

## Slide 55: Event-by-event fluctuations
X. Luo, Quark Matter 2015
M.A. Stephanov,
PRL107, 052301 (2011).
J-PARC
Theory
Event-by-event fluctuations of conserved charge:
Probe to search for the critical point
Enhancement of 4th-order fluctuations at low energies
Indications of the critical point?
 J-PARC-HI may answer that.

## Slide 56: J-PARCハドロン物理の高密度への展開
|S|>=3 hypernuclei
HI experiment
Neutron Star
Chiral restoration dilepton in p+A
p/K/p beam experiments
YN YY interactions
高密度（～中性子星コア）
Hard EOS
Exotic hadrons
Q+ Pentaquark
H-dibaryon
Exotic hadrons
(distinguish structure by production yield)
Hypernuclei
|S|<=2
通常原子核密度
太陽質量の２倍
⇒硬いEOS
Ｙ,Ｎ三体力?
Quark-hadron phase transition?
Kaonic nuclei：K-pp
中性子過剰ハイパー核
中性ハイパー核: nnL, nnLL
Strangelet (strange quark matter)
Collective flow
2-particle correlation (HBT)
Core Matter

## Slide 57: ハイペロン２粒子相関
STAR, PRL114 (2015) 022301
(Morita et al
PRC91 (2015) 024916)
Study of LL interactions from two-particle momentum correlation
Other YN, YY, YYN correlation measurements possible
    X- and W multiplicity = 0.6/0.03 at 10 AGeV
    Wp : K. Morita et al, Phys. Rev. C94 (2016) 031901
LL correlation function
QS+BB interaction
Nagara
STAR
STAR
Notes: Effective range and inverse of scattering length

## Slide 58
Talk in ALICE Week, Nov. 2017, Aleksi Kurkela

## Slide 59
Tidal deformability
during inspiral
Talk in ALICE Week, Nov. 2017, Aleksi Kurkela
How HIC
contributes to
EOS?

## Slide 60: さらなる高バリオン密度へ 新しい事象選択法 (preliminary)
pT of hadrons correlates with baryon density
  Cascade model calculation (JAM)
  A. Ohnishi, Y. Nara, M. Kitazawa, T. Sakaguchi, H. Sako, private comm.
Possibility of implementing an experimental trigger
Statistics-starved “rare event” selection feasible with high luminosity beam at J-PARC-HI

## Slide 61: Preliminary detector specifications
SVD
Pad size 40umx40um2 at 25cm
GEM tracker
Pad size (<=2x2mm2 at 2m)
MRPC-TOF
L=4m
Dt=60ps
RICH
Radiator ~0.5m
C5F12 g~15.8
  m: p>1.7GeV/c
  p: p>2.2GeV/c
  Npe = 33
EMCAL
PbWO4
15X0 (14cm), 0.8lint
  90% of 10GeV photon energy deposited
dE = 2.4%/√E + noise
Neutron detector
Charge veto counter + EMCAL(0.8lint)
or Plastic scintillator array
Muon Tracker
・Fe Absorber + MWPC (6-7 lint)

## Slide 62
3.2m
Neutron counter
EMCAL
ZCAL
Beam
RICH
4m
Muon Tracker
R=1m
Top
View
Toroid
coils
0.25m
0.5m
1.4m
0.65m
1.90m
TOF
SVD
ZCAL
4.4m
Centrality
MC + ZCAL
Multiplicity
counter
C5F12 radiator
p<3.4GeV/c
e-p separation
EMCAL (e,g ID)
PbWO4, 15X0
JHITS
m–p separation
Fe absorbers
+trackers
GEM trackers
Neutron detector

## Slide 63: Simulation for U86+acceleration in the RCS
Time [ms]
Code: ORBIT-3D
Steps:
(1) Single particle w/o SC
(2) Multi-particle w/ SC
● BM, QM, Sextuples are kept unchanged
as optimized for 1MW proton (for MLF).
Those can’t be changed pulse-to-pulse.
● rf patterns are differently used.
 Upgrades might necessary.
(may not be a big issue.)
Injection energy: 61.8 MeV/u
Extraction energy: 735 MeV/u
 (1) Successfully confirmed by
the single particle simulation.
rf patterns
(1)

## Slide 66: Charmed particles
c-c produced in the early stage of collisions
  D,J/y may be modified
  Probe of high density state
  J-PARC energies close to the production thresholds
  D (5.07 AGeV),J/y (4.77 AGeV)
  May be possible with increased beam energy 12 19 AGeV/c
  √s= 4.96.2GeV (U)
  Enhancement due to multi-step processes in A+A?
CBM Physics Book,
W. Cassing, E. L. Bratkovskaya and
A. Sibirtsev, Nucl. Phys. A 691 (2001) 753

## Slide 67: Exotic particles in HI collisions
Dibaryon
  HLLp-pp-p
  d*(2380)dp+p-
Kaonic nucleus
  K-ppLpp-pp
Resonances
  K*(892)pK
  D(1232)pp
  S(1385)Lp
  L(1520)pK-
  X(1530)Xp
  WLK-
  X-Lp-
Penta quarks
  Q+(uudd sbar)pKs
  Q+++(uuuu sbar)pp+p+
  Q0(uddd sbar)pK-
  Ns(uudd ubar)LK
  S5(udds ubar)Lp
  S5(uuds dbar)pK0bar
  π-pφn (udd ssbar)